## Slide 1: Chapter 18
an artificial vision device
© 2003 Thomson – Brooks/Cole
Phys2120 Spring 2017
© A. Dzyubenko
Direct Current Circuits

## Slide 2
Batteries provide a voltage with a fixed polarity, resulting in a direct current in a circuit
The current constant in magnitude and direction is called direct current, DC

## Slide 3: Sources of emf
The source that maintains the current in a closed circuit is called a source of emf (electromotive force)
Any devices that increase the potential energy of charges circulating in circuits are sources of emf
Examples include batteries and generators

## Slide 4: Emf and Internal Resistance
Therefore, the terminal voltage is not equal to the emf
A real battery has some internal resistance, that is resistance to the flow of charge within the battery
The emf  of a battery is the maximum possible voltage that the battery can provide between its terminals

## Slide 5: Emf and Internal Resistance
The real battery can be presented by an ideal resistance-free emf  in series with an internal resistance r
V across the battery is
V across the R is

## Slide 6: Internal Resistance and emf
ε is equal to the terminal voltage when the current is zero
    Also called the open-circuit voltage
R is called the load resistance
The current depends on both the resistance external to the battery and the internal resistance

## Slide 7
Resistors in Series

## Slide 8: Resistors in Series
When two or more resistors are connected end-to-end, they are said to be in series
The current is the same in resistors because any charge that flows through one resistor flows through the other
The sum of the potential differences across the resistors is equal to the total potential difference across the combination

## Slide 9: Resistors in Series
Potentials add:
  ΔV = IR1 + IR2 = I (R1+R2)
  ΔV = IReq Req = R1 + R2
    Consequence of Conservation of Energy
The equivalent resistance Req has the effect on the circuit as the original combination of resistors

## Slide 10: Equivalent Resistance: Series
  Req = R1 + R2 + R3 + …
The equivalent resistance of a series combination of resistors is the algebraic sum of the individual resistances.
It is always greater than any of the individual resistance.

## Slide 11: Equivalent Resistance – Series An Example
Four resistors are replaced with their equivalent resistance

## Slide 12: A piece of wire is used to connect points b and c . The brightness of bulb R1 (a) increases, (b) decreases, (c) stays the same? The brightness of bulb R2 (a) increases, (b) decreases, or (c) stays the same?
QUICK QUIZ

## Slide 13: R1 becomes brighter. Connecting a wire from b to c provides a nearly zero resistance path from b to c and decreases the total resistance of the circuit from R1 + R2 to just R1. The current passing through bulb R1 increases, causing this bulb to glow brighter. Bulb R2 goes out because essentially all of the current now passes through the wire connecting b and c and bypasses the filament of bulb R2.
QUICK QUIZ ANSWER

## Slide 14: With the switch in this circuit (figure a) closed, no current exists in R2 because the current has an alternate zero-resistance path through the switch. Current does exist in R1 and this current is measured with the ammeter at the right side of the circuit. If the switch is opened (figure b), current exists in R2. After the switch is opened, the reading on the ammeter (a) increases, (b) decreases, (c) does not change.
QUICK QUIZ

## Slide 15: (b). When the switch is opened, resistors R1 and R2 are in series, so that the total circuit resistance is larger than when the switch was closed. As a result, the current decreases.
QUICK QUIZ ANSWER

## Slide 16
Resistors in Parallel
  I = I1 + I2
Junction a

## Slide 17: Resistors in Parallel
The potential difference across each resistor is the same because each is connected directly across the battery terminals
The current, I, that enters a point (junction) must be equal to the total current leaving that point (junction)
  I = I1 + I2

## Slide 18: Resistors in Parallel, cont
The equivalent resistance Req has the effect on the circuit as the two resistors in parallel

## Slide 19: Equivalent Resistance – Parallel
Equivalent resistance is
The inverse of the equivalent resistance of two or more resistors connected in parallel is the algebraic sum of the inverses of the individual resistance
The equivalent is always less than the smallest resistor in the group

## Slide 20: With the switch in this circuit (figure a) open, there is no current in R2. There is current in R1 and this current is measured with the ammeter at the right side of the circuit. If the switch is closed (figure b), there is current in R2. When the switch is closed, the reading on the ammeter (a) increases, (b) decreases, or (c) remains the same.
QUICK QUIZ

## Slide 21: (a). When the switch is closed, resistors R1 and R2 are in parallel, so that the total circuit resistance is smaller than when the switch was open. As a result, the total current increases.
QUICK QUIZ ANSWER

## Slide 22: Problem-Solving Strategy, 1
When two or more unequal resistors are connected in series, they carry the same current, but the potential differences across them are not the same.
    The resistors add directly to give the equivalent resistance of the series combination
    Req = R1 + R2 + R3 + …

## Slide 23: Problem-Solving Strategy, 2
When two or more unequal resistors are connected in parallel, the potential differences across them are the same. The currents through them are not the same.
    The equivalent resistance of a parallel combination is found through reciprocal addition
    The equivalent resistance is always less than the smallest individual resistor in the combination

## Slide 24: Problem-Solving Strategy, 3
A complicated circuit consisting of several resistors and batteries can often be reduced to a simple circuit with only one resistor
    Replace any resistors in series or in parallel using steps 1 or 2.
    Sketch the new circuit after these changes have been made
    Continue to replace any series or parallel combinations
    Continue until one equivalent resistance is found

## Slide 25: Problem-Solving Strategy, 4
If the current in or the potential difference across a resistor in the complicated circuit is to be identified, start with the final circuit found in step 3 and gradually work back through the circuits
    Use ΔV = IR and the procedures in steps 1 and 2

## Slide 26: You have a large supply of lightbulbs and a battery. You start with one lightbulb connected to the battery and notice its brightness. You then add one lightbulb at a time, each new bulb being added in parallel to the previous bulbs. As the lightbulbs are added, what happens (a) to the brightness of the bulbs? (b) to the current in the bulbs? (c) to the power delivered by the battery? (d) to the lifetime of the battery? (e) to the terminal voltage of the battery? Hint: Do not ignore the internal resistance of the battery.
QUICK QUIZ 18.4

## Slide 27: (a) The brightness of the bulbs decreases (b) The current in the bulbs decreases (c) The power delivered by the battery increases (d) The lifetime of the battery decreases (e) The terminal voltage of the battery decreases
QUICK QUIZ 18.4 ANSWER

## Slide 28: Equivalent Resistance – Complex Circuit

## Slide 29: Kirchhoff’s Rules
There are ways in which resistors can be connected so that the circuits formed cannot be reduced to a single equivalent resistor
Two rules, called Kirchhoff’s Rules can be used instead

## Slide 30: Statement of Kirchhoff’s Rules
Junction Rule. The sum of the currents entering any junction must equal the sum of the currents leaving that junction
    A statement of Conservation of Charge
Loop Rule. The sum of the potential differences across all the elements around any closed circuit loop must be zero
    A statement of Conservation of Energy

## Slide 31: More About the Junction Rule
I1 = I2 + I3
From Conservation of Charge
Diagram (b) shows a mechanical analog of the junction rule

## Slide 32: Setting Up Kirchhoff’s Rules
Assign symbols and directions to the currents in all branches of the circuit
    If a direction is chosen incorrectly, the resulting answer will be negative, but the magnitude will be correct
When applying the loop rule, choose a direction for transversing the loop
    Record voltage drops and rises as they occur

## Slide 33: More About the Loop Rule
Traveling around the loop from a to b
In (a), the resistor is transversed in the direction of the current, the potential across the resistor is –IR
In (b), the resistor is transversed in the direction opposite of the current, the potential across the resistor is +IR

## Slide 34: Loop Rule
In (c), the source of emf is transversed in the direction of the emf (from – to +), the change in the electric potential is +ε
In (d), the source of emf is transversed in the direction opposite of the emf (from + to -), the change in the electric potential is -ε

## Slide 35: Junction Equations from Kirchhoff’s Rules
Use the junction rule as often as needed so long as, each time you write an equation, you include in it a current that has not been used in a previous junction rule equation
  In general, the number of times the junction rule can be used is one fewer than the number of junction points in the circuit

## Slide 36: Loop Equations from Kirchhoff’s Rules
The loop rule can be used as often as needed so long as a new circuit element (resistor or battery) or a new current appears in each new equation
You need as many independent equations as you have unknowns

## Slide 38: Problem-Solving Strategy – Kirchhoff’s Rules
Draw the circuit diagram and assign labels and symbols to all known and unknown quantities. Assign directions to the currents.
Apply the junction rule to any junction in the circuit
Apply the loop rule to as many loops as are needed to solve for the unknowns
Solve the equations simultaneously for the unknown quantities.

## Slide 39: Example

## Slide 40: RC Circuits:Charging a Capacitor
A circuit containing a series combination of a resistor and a capacitor is called an RC circuit

## Slide 41: RC Circuits
A direct current circuit may contain capacitors and resistors, the current will vary with time
When the circuit is completed, the capacitor starts to charge
The capacitor continues to charge until it reaches its maximum charge (Q = Cε)
Once the capacitor is fully charged, the current in the circuit is zero

## Slide 42
RC Circuits: Charging a Capacitor

## Slide 43: RC Circuits:Charging a Capacitor
Traveling the loop clockwise gives:
The initial current I0 in the circuit is
(current at t = 0)
The maximum charge (current I = 0) is
What is the time dependence of the charge and current?

## Slide 44: Time Dependence of Charge
Quantity RC is called the time constant  of the circuit and represents the time required for the charge to increase from zero to [1- e -1] = 0.632 of its maximum

## Slide 45
RC Circuits: Discharging a Capacitor

## Slide 46: Discharging Capacitor in an RC Circuit
When a charged capacitor is placed in the circuit, it can be discharged
    q = Qe-t/RC
The charge decreases exponentially
At t =  = RC, the charge decreases to 0.368 Qmax
    in one time constant, the capacitor loses about 63% of its initial charge
    e = 2.718…
    e-1 = 0.368…
    q=Qe-1

## Slide 47: Household Wiring

## Slide 48: Electrical Safety
Electric shock can result in fatal burns
Electric shock can cause the muscles of vital organs (such as the heart) to malfunction
The degree of damage depends on
    the magnitude of the current
    the length of time it acts
    the part of the body through which it passes

## Slide 49: Effects of Various Currents
5 mA or less
    can cause a sensation of shock
    generally little or no damage
10 mA
    hand muscles contract
    may be unable to let go of a live wire
100 mA
    if passes through the body for 1 second or less, can be fatal

## Slide 50: Ground Wire
Electrical equipment manufacturers use electrical cords that have a third wire, called a ground
Prevents shocks

## Slide 51
Ground Wire

## Slide 52: Ground Fault Interrupters (GFI)
Special power outlets
Used in hazardous areas
Designed to protect people from electrical shock
Senses currents (of about 5 mA or greater) leaking to ground
Shuts off the current when above this level

## Slide 53: Electrical Signals in Neurons
Specialized cells in the body, called neurons, form a complex network that receives, processes, and transmits information from one part of the body to another
Three classes of neurons
  Sensory neurons
    Receive stimuli from sensory organs that monitor the external and internal environment of the body
  Motor neurons
    Carry messages that control the muscle cells
  Interneurons
    Transmit information from one neuron to another

## Slide 54: Diagram of a Neurons

## Slide 55
A simple neural circuit